## Slide 1
Firmware Binary
Comparison Tool
Know exactly what changed between two firmware builds — where, in which function, and whether it was expected.
Demo · v1.0.0 frozen baseline · 16 October 2026
.bin · Intel .hex · .elf | GUI · CLI · HTML / CSV / JSON reports
Notes: Introduce the tool: a desktop and command-line utility for embedded firmware engineers. Goal of the demo: show how quickly we can answer 'what exactly changed between these two builds?'.

## Slide 2
Why a byte diff is not enough
Questions engineers actually ask before releasing firmware
MOTIVATION
Firmware Binary Comparison Tool · v1.0.0
2
Where did it change?
MCU addresses, not file offsets. BIN, HEX and ELF use different address views.
Was it expected?
Version strings, build timestamps and CRCs always change — real changes must stand out.
Which function?
Removing one call shifts all later code: hundreds of functions differ without being edited.
Which controller?
Is this image really for the STM32F411 / PIC32MX575 we expect?
▪ Generic diff tools show offsets and raw bytes — no regions, no expectations, no symbols.
▪ Manual review of hex dumps is slow and misses changes hidden behind code shifts.
▪ This tool answers all four questions in one view, and as a CI gate from the command line.
Notes: Set the scene with the four questions. Mention the watchdog example we will use later: a 3-line change produced 92,000 different bytes.

## Slide 3
What the tool does
Feature overview
OVERVIEW
Firmware Binary Comparison Tool · v1.0.0
3
Byte comparison
BIN / HEX / ELF by MCU address, size changes, gap fill, 64 MB in ~0.1 s
Regions & expectations
Named regions, expected areas (version, CRC …), EXPECTED vs UNEXPECTED verdict
Functions & modules
ELF / linker map symbols, relocation-aware: real edits vs side effects
Controller identification
STM32F411RET, PIC32MX575F512L … with evidence and confidence
Hex viewer & memory map
Synchronised hex view, navigation, search, filters, visual block map
Reports & CLI
HTML, CSV, JSON; firmware-diff with CI exit codes
Notes: Six capability areas. Everything runs locally, needs only Python 3.11, and never modifies the firmware files.

## Slide 4
Architecture
GUI-independent engine shared by GUI, CLI and tests
DESIGN
Firmware Binary Comparison Tool · v1.0.0
4
Notes: Layers: formats parse and validate files; core holds the engine (IntervalSet-based differences, analysis, symbols, controller detection); session orchestrates; GUI, CLI and reports are thin front ends. Standard library only.

## Slide 5
How a comparison runs
Five steps — the expensive one runs once
DESIGN
Firmware Binary Comparison Tool · v1.0.0
5
▪ Union of addresses: bytes present in only one image are differences — nothing is silently ignored.
▪ Hierarchical scan: 64 KiB chunks, identical areas skipped at memcmp speed, differences stored as runs.
▪ Instant re-analysis: editing regions, expected areas or symbol files does not re-compare bytes.
Notes: Explain the union-of-addresses idea and the run-based storage that keeps large images fast.

## Slide 6
Step 1 · Select the firmware
Drop zones, base address, symbol files, configuration
DEMO
Firmware Binary Comparison Tool · v1.0.0
6
▪ A / B cards: click or drop a file; name, size, SHA-256, format, address range
▪ Base address for raw .bin files
▪ Controller identified automatically
▪ Symbol files (ELF / .map) unlock function-level results
▪ Compare runs automatically → Summary
Notes: Live: drop Analysis_Board_Firmware.hex (old) and the watchdog-commented build (new), load both ELFs as symbol files. Point out the controller row: STM32F411RET, Cortex-M4 with FPU.

## Slide 7
Step 2 · The answer at a glance
Verdict, key numbers and what changed
DEMO
Firmware Binary Comparison Tool · v1.0.0
7
92,007 bytes differ (76 %)
…because one call was removed and all later code shifted.
2 functions modified
6 symbols removed
peripheralInit and main lost their watchdog calls; the IWDG driver was dropped by the linker.
Notes: Key message: the byte count is huge, the real change is tiny. The 'What changed' list shows exactly the watchdog edit.

## Slide 8
Real edits vs side effects
Relocation-aware function comparison
HIGHLIGHT
Firmware Binary Comparison Tool · v1.0.0
8
Before
350 'modified'
After
2 modified · 6 removed
▪ Calls (BL / JAL) and pointers are decoded in both builds
▪ Same target symbol → RELOCATED, not an edit
▪ 762 side effects listed separately
▪ ARM Thumb-2 and MIPS32 (PIC32)
Notes: This is the key innovation. Removing a call shifts later code, changing branch offsets and literal pools everywhere. The tool resolves each reference to symbol+offset in both builds and only counts real content changes.

## Slide 9
Side effects stay visible
Relocated / moved symbols on their own filter
HIGHLIGHT
Firmware Binary Comparison Tool · v1.0.0
9
▪ RELOCATED: only call targets / pointers changed
▪ MOVED: identical code at a new address
▪ LIKELY RELOCATED: references to unnamed data — listed for review, never hidden
▪ Module view from linker map files (motor.o, uart.o …)
Notes: Nothing is hidden: switch the filter to see the 762 side effects and their notes.

## Slide 10
Hex comparison viewer
Synchronised, virtualised — scrolls MB-sized images instantly
DEMO
Firmware Binary Comparison Tool · v1.0.0
10
▪ First / prev / next / last difference
▪ Go to address or file offset
▪ Hex search in A, B or both
▪ Filters: diffs only, region, block size
▪ Status bar: offsets, region, block, function
Notes: Double-click peripheralInit in the function list to jump here. Show n / p keys and the 1-byte table layout (Address | A | B | Status).

## Slide 11
Regions and expected changes
Version, timestamp and CRC are allowed to change — nothing else is
DEMO
Firmware Binary Comparison Tool · v1.0.0
11
Summary: 22 expected bytes (version, timestamp, git hash, CRC) are separated from 14,179 unexpected ones.
Regions: Bootloader and Calibration show EXPECTED CHANGE only; Application and Diagnostics really changed.
Notes: Example project with Bootloader / Application / Calibration / Diagnostics and expected areas for version, build timestamp, git hash and CRC. Bootloader and Calibration are EXPECTED CHANGE only; Application and Diagnostics have unexpected changes.

## Slide 12
Changed blocks and memory map
Where the changes are — as a table and as a picture
DEMO
Firmware Binary Comparison Tool · v1.0.0
12
Every block with size, class, region, file offsets and the function it falls in; sortable and filterable.
Memory map: red = unexpected, amber = expected only. Click any cell to open the hex viewer there.
Notes: Blocks can be sorted by address, size or region and filtered by class or size; each row names the function. The map: red = unexpected, amber = expected only; click a cell to open the hex viewer.

## Slide 13
Configuration
Reusable project files: regions, expected areas, settings
SETUP
Firmware Binary Comparison Tool · v1.0.0
13
▪ Add / edit / remove / reorder
▪ End address or +size
▪ Validation: ranges, duplicates, overlaps
▪ Gap fill for sparse HEX vs full BIN (opt-in)
▪ Saved as JSON, used by GUI and CLI
Notes: Expected areas are never assumed — the engineer configures them explicitly.

## Slide 14
Controller identification
Exact part from symbols, family from the image layout
HIGHLIGHT
Firmware Binary Comparison Tool · v1.0.0
14
▪ PIC32MX575F512L from the XC32 map — 512 KB flash, 100 pins
▪ STM32F411RET from ELF debug info — Cortex-M4F, 512 KB, LQFP64
▪ HEX / BIN only: family from flash layout, config words, vector table
▪ Warning if A and B target different controllers
Notes: Every identification lists its evidence and confidence. An application at 0x08040000 is flagged as sitting behind a bootloader.

## Slide 15
Metadata · Checksums · ELF
Supporting analysis
DEMO
Firmware Binary Comparison Tool · v1.0.0
15
Heuristic metadata: version, build date/time, git, product, board
CRC-32 / CRC-16 / SHA-256 over file, image, region or range
ELF sections, build info and symbol changes
Notes: Metadata detection is heuristic and says so. Checksums never assume the firmware's own CRC algorithm.

## Slide 16
Command line & CI
Same engine, scriptable — exit codes gate a release
AUTOMATION
Firmware Binary Comparison Tool · v1.0.0
16
Exit codes
▪ 0 identical or expected changes only
▪ 1 unexpected changes
▪ 2 error (missing / malformed file, bad config)
▪ --report / --csv / --json
▪ --symbols-a / --symbols-b
▪ --regions / --ignore
▪ --fill, --merge-gap, --checksum
Notes: Show the one-line CI usage: firmware-diff old.bin new.bin --regions project.json --report r.html. A non-zero exit code fails the pipeline on unexpected changes.

## Slide 17
HTML engineering report
Self-contained, printable, shareable
OUTPUT
Firmware Binary Comparison Tool · v1.0.0
17
▪ Firmware A / B information incl. controller
▪ SHA-256 hashes, overall summary, memory map
▪ Region comparison
▪ Changed blocks with function names
▪ Expected and unexpected changes
▪ Function and module changes, side effects
▪ Metadata differences, ELF comparison, timestamp
▪ CSV exports for blocks and functions; JSON summary
Notes: Open docs/sample_comparison_report.html in a browser to show the full report.

## Slide 18
Quality and performance
Verified on synthetic and production firmware
QUALITY
Firmware Binary Comparison Tool · v1.0.0
18
84
automated tests
0.1 s
64 MB comparison
2
production firmware families
0
runtime dependencies
▪ Engine: randomised tests against a naive byte-by-byte reference; interval algebra against Python sets.
▪ Formats: malformed / truncated HEX and ELF, overlapping records, files verified unmodified.
▪ Functions: real Thumb-2 and MIPS32 machine code, aliases, linker labels, renamed compiler symbols.
▪ Production: STM32F411 watchdog change → exactly 2 modified + 6 removed; PIC32MX575 release diff.
▪ GUI: smoke test drives the real window — load, compare, tabs, hex navigation, filters, search.
Notes: Mention the freeze: v1.0.0 baseline with a SHA-256 manifest of every file (docs/FREEZE_v1.0.0.md).

## Slide 19
Limitations and next steps
v1.0.0 is frozen — candidates for the next version
ROADMAP
Firmware Binary Comparison Tool · v1.0.0
19
▪ Heuristics: metadata and controller identification are best-effort, with evidence shown
▪ Decoding: MOVW/MOVT, microMIPS / MIPS16e and RISC-V not decoded yet
▪ Maps: GNU ld and XC32 only (IAR / Keil: use their ELF)
▪ Formats: no Motorola S-record yet
▪ Same-size MODIFIED can be a side effect of header / struct changes
Possible next steps
▪ S-record and IAR / Keil map support
▪ RISC-V and MOVW/MOVT reference decoding
▪ Batch / folder comparison of release sets
▪ Git integration: compare two tags directly
▪ Packaged installer (PyInstaller scripts ready)
Notes: Invite feedback on priorities for the next version.

## Slide 20
Thank you — questions?
Byte-exact comparison · regions & expectations · real edits vs side effects · controller identification
Run: python firmware_compare_gui.py · python firmware_diff.py old.bin new.bin --report r.html
Docs: docs/Firmware_Binary_Comparison_Tool_Design_v1.0.docx · README.md · docs/FREEZE_v1.0.0.md
Notes: Close: where to find the tool, the design document and the freeze manifest.